## Slide 1: Development of a model order reduction library for an Android-based FEM app
Cakal, Karakaya, Meßmer
Technische Universität München
Software Lab
Department of Civil, Geo and Engineering
Munich, 02. August 2018

## Slide 2: Why using FEM on a Smartphone?
Two Major Fields of Application
Teaching Tool
Helps students to understand the workflow of FEM
Solutions can be obtained easily
Portable Computational Support
Analyse structure on site
Provides first rough estimation of the problem
www.Colourbox.de
www.Colourbox.de

## Slide 3: Where did we start?
We started from the very beginning…
Our Task is…
Create a 2D - FEM framework that runs on a wide range of Android devices
Guide user intuitively from Geometry Creation to Post-Processing
Provide a Model Order Reduction Method to solve models more efficiently and be able to solve more complex (bigger) systems
BE FAST

## Slide 4
Milestones
FEM Package
June
September
Try C++ Option
Go for 2 weeks
Anything Goes Wrong?
Start Java Library
Finish Fem Package
Fine?
Finish & Test
C++ Library
Implement MOR Methods
August
WE ARE HERE

## Slide 5
How do we use C++ Code?
Android App
Java
Native Libs
C++
NDK
SDK
JNI
Native Development Kit
Compiler, linker
Builds for ARM architecture
Generates native libs
Java Native Interface
Interaction with native libs
Allows access to C++ classes, methods, members

## Slide 6
How do we use C++ Code?
Android
App (.apk)
Android
Activities/Fragments
(.java)
FEM Package
(.h / .cpp)
Native Libs
(.so)
NDK
JNI
Outcomes;
Enhanced control on memory management
Faster FEM Calculations
Cross-platform development
Easy future implementations of FEM Package

## Slide 7
FEM Package
Utilities
Geokernel
Post Processing
Femkernel
Mathkernel
Just the solvers and linear algebra libraries
It has an interface with FEM Package
Can be changed

## Slide 8
FEM Package
Utilities
Geokernel
Post Processing
Femkernel
Mathkernel
Solves the reduced equation system
Technically the same job but decreased complexity.
MOR Package
Reduce Matrices
Decrease complexity
2
3
4
1

## Slide 9
Geometry
Json
FEM Package (C++)
Json File Storage
Java App
Mesher
Solver
Material
Mesh
Json
BC’s
Results
Json
Android App Workflow

## Slide 10
Work Plan
  Done
    Get familiar with the Android Development Environment
    Construct Android application layout
    Make rendering framework available
    Implement the FEM-Package (C++)
    Add some features to the application (Mostly About Visualization)
  To - Do
    Implement a Model Order Reduction method
      First deploy chair’s existing code into developed FEM flow and make performance test
        If time permits go experimental
    Add further features to the application (e.g. geometry types, elements types… )